 DM9051A OTP GUI Spec.
v02

---
Dashboard
Device List :
Dev ID	Meta data	Status	Action	Total Progress
Dev A	COM5:115200,N,8,1	Profile err
Dev B	COM6:115200,N,8,1	Flash
…..
Profile
Start
0%
Profile
Stop
80%
80%
Messages
12/06 16:28 COM 5: Received Profile,
12/06 16:29 COM 6 Finish downloading profile
12/06 16:30 COM 6 Flashing...
  …
Save
Flash Dev 1: VComm3, 115200, N, 8, 1
File
View

---
開發階段有menu 可以debug，  Release 拿掉
頁面名稱
Dashboard
下載/停止 燒錄動作
Device List :
Dev ID	Meta data	Status	Action	Total Progress
Dev A	COM5:115200,N,8,1	Profile err
Dev B	COM6:115200,N,8,1	Flash
…..
Profile
Start
0%
Profile
Stop
80%
80%
可以滑動瀏覽其他 VComm
Profile 按鈕，設定 Profile 內容，進入下一頁
Messages
12/06 16:28 COM 5: Received Profile,
可以滑動瀏覽其他 messages
12/06 16:29 COM 6 Finish downloading profile
12/06 16:30 COM 6 Flashing...
  …
Save
Save log messages as report file, 用日期爲檔名
Flash Dev 1: VComm3, 115200, N, 8, 1
View

---
Profile：Dev B
Import...
File Name: 1215.cfg
Dev B：COM6:115200,N,8,1
Export...
Field	Value	Editable
Mac Addr.	FF:FF:FF:FF:FF:FF	Y
Auto Load Control.	0xFF	Y
Vendor ID	0x0A46	N
Product ID	0x9051	N
Pin Control	0x0000	N
Wake-up Control	0x0157	N
Control 3	0x0000	N
Cancel
Confirm

---
Mouse click後可以直接修改，Value = FF 可以修改，其他不能修改（Fused）
Profile：Dev B
Import...
File Name: 1215.cfg
Dev B：COM6:115200,N,8,1
Total 18 Bytes
Export...
Field	Value	Editable
Mac Addr.	FF:FF:FF:FF:FF:FF	Y
Auto Load Control.	0xFF	Y
Vendor ID	0x0A46	N
Product ID	0x9051	N
Pin Control	0x0000	N
Wake-up Control	0x0157	N
Control 3	0x0000	N
Mouse click後可以直接修改，Value = FF 可以修改，其他不能修改（Fused）
Cancel
Confirm
Confirm 後寫入燒錄器
Cancel 取消所有表格的修改

---
Porfile Format
Name	Start	Len	Example Hex Value
MAC Addr	0x0	0x6	0x02 0x42 0x6a / 0x87 0xe8 0x45
Auto Load Control	0x06	0x2	0x5555
	0x20
	0x30

---
文件結束
以下素材備用區

---
開發階段有menu 可以debug，  Release 拿掉
Virtual device 的附屬說明
Flash Dev 1: VComm3, 115200, N, 8, 1
Device
Profile
Progress :
66/100
Total
只有顯示一個 Result
Result
OK O
Fail X
Messages
12/06 16:28 Start downloading profile
12/06 16:29 Finish downloading profile
12/06 16:30 Flashing...
Save
Save log messages as report file
View

---
Field	Value
Mac Addr.	3C:52:67:12:E3:46
Mac Auto Inc.	Y
Batch Size	100
CMD	0xF933AAC0
Row Data Bytes	32
Row Data Source	Flash_1212.data
Dev B：COM6:115200,N,8,1
Profile：Dev B
Edit
按下開始編輯
Cancel
Save
Cancel
Save
接受修改
放棄修改
	0	1	2	3	4	5	6	7
1	01	CA	EE	23	BF	69	80	EE
2	34	23	BF	69	80	EE	66	DE
3	33	23	A2	69	80	EE	FC	A1
4	21	0B	7D	69	80	95	44	98
修改